## Slide 1
Wtyczka zasilania routera.
Dobierz odpowiednią wtyczkę.
Najczęściej plus jest wewnątrz (sprawdź to).
To power the router.
Choose the right plug.
Most often the plus is inside (check it).
Gniazdo zasilania, do którego podłączasz oryginalny zasilacz Routera. Dobierz odpowiednie do zasilacza routera.
Power socket where you connect the original Router power supply.
Choose the appropriate one for your router power supply.
Dowolna przetwornica DC-DC step DOWN. Zwykle routery zasilane są napięciem 9-24V. Zanim ją zamontujesz, ustaw potencjometrem napięcie wyjściowe 5V do zasilania ESP32.
Any DC-DC converter step DOWN. Routers are usually powered by 9-24V. Before you mount it, first set the output voltage of 5V with a regulator to power the ESP32.
GPIO15
3.3V pin
GPIO15 (button)
3.3V pin
GPIO14
330 om
GPIO14 (LED)
GPIO5 (Relay)
MicroUSB for ESP32 power 5V

## Slide 2
To ESP32 USB
GPIO5
DC-DC step down set to 5V output
INPUT router power supply
OUTPUT to router
+
-
Signal
HIGH
enable
relay